## Slide 1: name: nowshin mehanaz id: 19201019 dept:civil course code:ce3131
TOPIC: SECONDARY CONSOLIDATION SETTELEMENT

## Slide 2
Secondary Consolidation
The secondary consolidation happens after the primary compression, even after the excess hydrostatic stress has dissipated. Some of the settlement happens in the soil after primary consolidation and that is termed as secondary compression and it is usually time dependent. In sandy soil, this type of settlement is negligible. But in the soil like clay and peat, it is more significant. The secondary consolidation is otherwise called as secondary compression.

## Slide 3
What is secondary consolidation caused by
The reduction in volume of a soil mass caused by the application of a sustained load to the mass, due principally to the adjustment of the internal structure of the soil mass after most of the load has been transferred from the soil water to the soil solids.

## Slide 4
The secondary compression settlement (creep) can be estimated from the secondary compression index Cɛα = Cα/(1 + e0), where Cα is the coefficient of secondary compression and e0 is the initial void ratio.