## Slide 1: Namw name: nowshin mehanaz id: 19201019 dept:civil course code:ce3115
TOPIC:BASICS OF DOUBLY REINFORCED BEAM

## Slide 2: What is doubly reinforced concrete beam? A reinforced concrete beam with steel reinforcement both in tension and compression zone is called a doubly reinforced beam.

## Slide 3: What is the difference between doubly reinforced concrete beam and singly reinforced concrete beam? A beam that is reinforced in the tension zone only is called a singly reinforced concrete beam, whereas a doubly reinforced concrete beam is reinforced on both tension and compression faces.

## Slide 4: What is doubly reinforced beam and why is it used? Doubly reinforced beam is provided to increase the moment of resistance of a beam having limited dimensions. Minimum compression reinforcement is provided to hold the Shear Reinforcement (stirrups) in position and for increasing the ductility of beam.

## Slide 5: Doubly reinforced beam 1. Beams reinforced with steel in compression and tension zones are called doubly reinforced beams. This type of beam will be found necessary when due to head room consideration or architectural consideration the depth of the beam is restricted. 2. he beam with its limited depth, if reinforced on the tension side only, may not have enough moment of resistance, to resist the bending moment. 3. By increasing the quantity of steel in the tension zone, the moment of resistance cannot be increased indefinitely. Usually, the moment of resistance can be increased by not more than 25% over the balanced moment of resistance, by making the beam over-reinforced on the tension side.

## Slide 6
Besides, this doubly reinforced beam is also used in the following circumstances:
The external live loads may alternate may occur on either face of the member.

## Slide 7
For example:
A pile may be lifted in such a manner that the tension and compression zones may alternate.
The loading may be eccentric and the eccentricity of the load may change from one side of the axis to another side.
The member may be subjected to a shock or impact or accidental lateral thrust.

## Slide 8
Design procedure for doubly reinforced beam
Step 1
Determine the limiting moment of resistance for the given c/s(Mulim) using the equation for singly reinforced beam
Mulim = 0.87.fy.Ast1.d [1 – 0.42Xumax]
Or
Balanced section
Ast1 = (0.36.fck.b.Xumax)/(0.87fy)
Step 2
If factored moment Mu > Mulim, then doubly reinforced beam is required to be designed for additional moment.
Mu – Mulim = fsc.Asc (d – d’) [fsc value from page no. 70]

## Slide 9
Step 3
Additional area of tension steel Ast2
Ast2 =Asc.fsc/0.87fy
Step 4
Total tension steel Ast, Ast = Ast1 + Ast2

## Slide 10
Doubly reinforced beam
DOUBLY REINFORCED BEAMS